## Slide 1: Gas Flaring Philosophy -
Approval requirements and considerations for future MCP design

## Slide 2: Flaring Approval Requirements
CABGOC continues to work toward reducing routine and non-routine flaring in Blocks 0/14.
ALNG will significantly increase the economic value of gas to the Concession
Multiple Standards require reducing and eliminating continuous flaring
      CVX Global Upstream Gas Flaring and Venting Environmental Performance Standards
      World Bank Global Gas Venting and Flaring Reduction (CVX is a member)
      Concession Extension Agreement May 2004
      BOEMRE (formally MMS) Code of Federal Regulations (CFR)
      Ministry of Petroleum has commented that eliminating flaring will be a priority in the future, perhaps a requirement where failing to comply may result in fines.

## Slide 3: Flaring Approval Requirements
Provide an increased level of management and stewardship to our flaring events
Approval for certain flaring events will be reviewed and granted on a case-by-case basis
Requirements are provided for both Existing and New (MCP) facilities.
Certain flaring events will have to be approved by the Operations Manager or General Manager of Operations.

## Slide 4: Non Routine Flaring (Existing Facilities) – Upset Conditions and Preventive Maintenance
Scenario | Approval Required
2 days or less | No Approval Required
Longer than 2 days but less than 30 days | Operations Manager *
Longer than 30 days | GM Operations * †
† Other Notifications may be required
* Considerations for approval will include, in addition to duration, several factors (e.g. safety, flare rate, reservoir management, other operational issues)

## Slide 5: Routine Flaring# (Existing Facilities)
Scenario | Approval Required
Less than 2 MMCFPD (offshore, per flare point) Less than 50 MCFPD (onshore, per flare point) | No Approval Required
Greater than 2 MMCFPD (offshore, per flare point) Greater than 50 MCFPD (onshore, per flare point) | Operations Manager and GMO*†
† Other Notifications may be required
* Considerations for approval will include, in addition to duration, several factors (e.g. safety, flare rate, reservoir management, other operational issues)
# Routine Flaring Excludes pilot and purge flare volumes

## Slide 6: New Facilities
Flare Type | Basis of Design*
Routine | Zero flare of associated gas †
Non Routine – Upset Conditions and Preventive Maintenance | Flaring allowed up to 48 hrs without impacting production. After 48 hrs Zero Flare. (Economic evaluation of sparing vs. prod curtailment required)
* Deviation from these BOD standards requires project DRB/DE and MD approval
† Routine Flaring Excludes pilot and purge flare volumes

## Slide 7: New Facilities – Other Considerations
Projects and Operations need plans in place to minimize downtime by having sufficient warehouse spares and/or installed spares to address equipment problems in the shortest window possible. Start up and operational spares to be in place before commissioning.
MCP needs to deliver their projects with the appropriate service contracts. These need to be in place before commissioning as our leverage decreases substantially after that.
The standardization of equipment affords many operational benefits. When specifying equipment and developing bid strategies, the development of an Approved Vendor List by MCP, with SBU input, and with clear processes for managing change to this list will help drive greater standardization.
Sparing philosophy should be driven by RAM studies, ECA’s and corresponding economic evaluations to ensure future production impacts are considered.